## Slide 1: ENGI 301 Froggy Racer Proposal
10/ 14 /2021
Oscar D. Soto

## Slide 2: Background Information
Goal: Make a multiplayer clicker game where the objective is to get your frog across the water lily field as fast as possible
Builds off the “Whack-a-Mole” and “PocketBeagle Arcade Machine” projects
    https://beagleboard.org/p/beaglefriends-octavosystems/whac-a-mole-game-with-pocketbeagle-738a4c
    https://beagleboard.org/p/fdm3/pocketbeagle-arcade-machine-ee661e
Improves on existing projects by introducing:
    Multiplayer functionality - play a friendly, competitive game where you race your frogs and test your ability to click fast

## Slide 3: System Block Diagram
Adafruit 7-segment LED Backpack
I2C1.SCL hub
I2C1.SDA hub
I2C1.SDA
AIN1 (1.8V)
PocketBeagle
GPIO57
I2C1.SCL
PRUO.2
PRUO.3
PRUO.5
Rotary Potentiometer
Arcade Button 1
Arcade Button 2
LED1 – Green
LED2 - Red
Toggle Switch
AINO (1.8V)
PRUO.4
SPIO
Piezo Speaker
LCD Screen
uUSB connector
USB1.VIN
USB1.DN
USB1.DP
USB1.ID
GND
USB Speaker

## Slide 4: Power Block Diagram
PocketBeagle
3.3V
Vout
uUSB Host Connector
5 V
Rotary Potentiometer
Toggle Switch
Adafruit 7-segment LED Backpacks
Arcade Button 1
Arcade Button 2
3.3 Volts
5 Volts
1.8 V
USB speaker
1.8 Volts

## Slide 5: Components / Budget
Component | Need to Buy | Cost
2.2" 18-bit color TFT LCD display with microSD card breakout – HX8340BN PRODUCT ID: 797 https://www.adafruit.com/product/797 | 1 | $29.95
Mini External USB Stereo Speaker PRODUCT ID: 3369 https://www.adafruit.com/product/3369 | 1 | $12.50
Arcade Button with LED - 30mm Translucent Red PRODUCT ID: 3489 https://www.adafruit.com/product/3489 | 1 | $2.50
Arcade Button with LED - 30mm Translucent Blue PRODUCT ID: 3490 https://www.adafruit.com/product/3490 | 1 | $2.50