## Slide 1: ENGI 301 Pokey Clicker Proposal
10/ 05/2021
Oscar D. Soto

## Slide 2: Background Information
Goal: Make a multiplayer clicker game where the objective is to click a button as many times as possible in under 10 seconds
  Builds off the “Whack-a-Mole” PocketBeagle game
    https://beagleboard.org/p/beaglefriends-octavosystems/whac-a-mole-game-with-pocketbeagle-738a4c
Improves on existing project by introducing:
    Multiplayer functionality - play a friendly, competitive game like “Pokey Pummel” from Mario Party

## Slide 3: System Block Diagram
Adafruit 7-segment LED Backpack
Adafruit 7-segment LED Backpack
I2C1.SCL hub
I2C1.SDA hub
GPIO48
I2C1.SDA
AINO (1.8V)
PocketBeagle
GPIO57
I2C1.SCL
PRUO.2
PRUO.3
PRUO.5
PRUO.6
GPIO58
Rotary Potentiometer
Tactile Button 1
Piezzo Speaker
Tactile Button 2
LED1 - Red
LED2 - Red
Toggle Switch
LED3 - Green

## Slide 4: Power Block Diagram
PocketBeagle
3.3V
Vout
uUSB Host Connector
3.3 V
Rotary Potentiometer
Toggle Switch
Adafruit 7-segment LED Backpacks
Tactical Button 1
Tactical Button 2
3.3 Volts

## Slide 5: Components / Budget
Component | Need to Buy | Cost
Large Solderless Breadboard PRODUCT ID: 443 https://www.adafruit.com/product/443 | 1 | $19.95
Adafruit 0.56" 4-Digit 7-Segment Display w/I2C Backpack - Red PRODUCT ID: 878 https://www.adafruit.com/product/878 | 1 | $9.95
Breadboard-friendly SPDT Slide Switch PRODUCT ID: 805 https://www.adafruit.com/product/805 | 1 | $0.95